User Manual  WIFI smoking detector Camera

First of all, thank you for using our company's products! Please read this manual before usage. In order to serve you well, the content of this user manual may be changed. Due to the change of the product performance and function , please contact us!

Product Introduction

This product is the first smoking detector camera with WIFI function  and high definition digital video cameras, TF card memory, to take high-definition video photos and high quality, this product is easy to operate, cabinet and delicate, beautiful and practical, easy to carry, is security, education, family life in areas such as the necessary utility, favored by the users.. Please refer to the appearance and button of this product.（Picture0）

swith,  usb charging port  Reset.(restore factory settings),   lens

Instruction for quick operation of network

This product is a HD (720P),25pfs, network surveillance smoking detector camera with internal micro SD card and a multi-functional high-tech product with functions of video recording, photographing, motion detection, alarm, APP real-time monitoring . It  has functions of 2 megapixel HD recording. Also support multi-language voice time reporting. It supports up to64GB micro SD card, uninterruptible long-time work and with APP convenient control. Moreover, it works as the best anti-theft and evidence-gathering tool with hidden camera.

I-APP software download

For Android phones, please search in Google Play :P2PLiveCam  to download the APP.

For iphone, please search in App Store:P2PliveCam to download the APP.

II-WIFI connection method one

1. push the switch to the ON , then the camera is turned on , and then red indicator light will flickering, which means the camera WIFI signal is opened）

2. turn on the WIFI on the smart phone . Run APP software that is downloaded and installed in your mobile phone. (The specific operation steps are shown as below pictures.)

Step 1（Run)     Step2（click） Step3（Click)

Step4（Input the UID number or scan the QR code that under back of the camera

Step5（Click to choose the available WIFI signal from your home router and input the password，Click）
3.After you connect the WIFI successfully,  you will be able to see the live video on the APP.

4.When the camera is connect successfully to your home router WIFI , the red indicator light will keep on and blue indicator light flickering.

III-WIFI connection method two

1. Then turn on the smoking detector camera（30 seconds later, blue indicator light start flickering, then the camera is turned on , and 30 seconds later the red indicator light will  flickering, which means the WIFI signal is opened）

2.Turn on the WLAN of your mobile. Then use your mobile to search the WIFI signal(WIFI name is the UID number on the camera ) sended out by this camera, and input the password to connect.(You need wait about three minutes to connect.)

4.After your mobile connect to the WIFI signal(sent out by this camera). Then you open the APP, then click  to search the camera ,then click   .

5. long click ,then click  , click . Select the SSID then input the password .click .

IV-Point-to-point AP direct connection(when you are in your home, and do not need the internet to control the camera, you can just connect your mobile with the WIFI sent out by the camera to control the camera in your home.)

1. power on the camera, then search the WIFI signal(WIFI name is the UID number of camera) sent out by the camera with your mobile,  and input the password to connect to this WIFI signal( It takes about three minutes to finish connection)

2. After your mobile connect to the WIFI signal sent out by the camera, then open the APP, click ,  then you can control the camera on your APP.

V-Screen shot, video recording and alarm

1.In the APP, open the live video as below picture, you can see on the top of  the screen with“720P, 480P” this two options, you can choose according to your own preference. Also you can adjust the color contrast degree and brightness. ,here from left to right respectively represent the function: monitor, photograph, video recording, left/right, up/down. By clicking “photograph” or “video recording”, the images or videos will be saved in the phone memory (as shown below).

2.Long press as below the “Cam” , to start more setting options.

3. Advanced configuration(To remotely change basic functions of the device)

PC operation guide

1. Install the search tool (which in the disc)  on the computer. (Note: administrator setting can only be made within LAN).

2.Click  to display the devices connected to network (as below)

3.Double click the searched IP. Enter in the next page to type in user name (admin) and click to confirm it. (Note: the original user name is admin, no need password)

4. Enter in setting page after completing the above steps. Download the plug-in and select a language for first use (click

to download and install).

5. Click

again to enter in setting page (as shown below).

6. Click  to start setting (as shown below)

- System management setting: to select the item to be set (as shown below).

Main function description

- Time setting

Open system management page——click time setting——select time zone——synchronize with host ——save.

2. Administrator password setting

Open “change password” ——type in the new password——confirm the new password——save.

3.Change the password of device (original password: 8888)

Open “network setting” ——P2P setting——type in the new password——save——return to system management to reboot the device. (it can also be set remotely by APP).

4.Alarm setting

Open “alarm setting” ——start alarm setting——click IP Camera built-in——select the required sensitivity. (Option 6 is suggested)

5. SD card setting

SD card should be formatted for the first time to insert——enter in SD card setting to select the needed function before setting other functions.

6. View the content of SD card
   method 1：Plug out the card and read with a card reader.

method 2：IE client——setting——SD card recording——SD files——select the file to download .
   .

Specifications

| Pixl | 2.0 megapixel CMOS |
| --- | --- |
| Resolution | 720P |
| Video format | ASF/AVI |
| Frames | 30 |
| View angle | 90° |
| Distance of motion detection shooting | 6 m straight-line distance |
| Power supply | 3.7V Li-battery |
| Continuous recording time | 2 hours |
| Compressed format | H.264 |
| Sound recording range | 5㎡ |
| Power consumption | 240mA/3.7V |
| Storage temperature | -20-80℃ |
| Operating temperature | -10-60℃ |
| Operating humidity | 15-85%RH |
| Type of memory card | Micro SD card |
| Maximum capacity of memory card | 64GB |
| Play software | VLCPlayer/SMPlayer |
| Computer operation system | Windows/Mac OS X |
| Mobile phone operation system | Android/iOS |
| Web browser | IE7 and above,chrome,Firefox safari.etc |
| support limited pieces client software online at same time | Can support 4 client software online the same time |

FAQ

1. Remote control is not enough.

Please select the most suitable definition according to the current network environment.

2.SD card cannot save files.

SD must be formatted for first use.

3.The device cannot be connected to network.

Please select the proper connection method according to the network nature.

4.The video in SD card cannot be played fluently on APP.

It is due to different decoding capacity of mobile phones. You can adjust the definition of recording device to fit your mobile phone.

5.The passwords are forgotten.

Directly click the reset key of device for 10 seconds to restore factory settings.

Precautions

Use occasions: please strictly comply with relevant state decrees and do not use it any other illegal purposes at your own risks.

Software upgrade: to achieve better product performance, the manufacturer will make continuous improvement to the software. This product is designed for convenient software upgrade by customers. Please ask your local distributor for the information and upgrading method of latest version of software.

Working temperature: please use it under natural temperature. Do not operate it under a temperature that is not adapted for human body.

Working humidity: please use it under an environmental humidity that is suitable for human life. Do not put the product in a moist working environment since the product is not designed with waterproof function.